## Slide 1: Foras Promineo Software

## Slide 2: What is a Cubesat?
CubeSats are a class of small satellites (generally satellites less than 500 kg) which are standardized around a volumetric unit, a 10 cm cube, or 1U (about 1 kg)
CubeSats currently range in size from 0.5U (about 0.5 kg) to 12U (about 24 kg)
Based on mass, CubeSats also fall in the categories of nanosatellite (1–10 kg) and microsatellite (10–100 kg)
Many different organizations are making and operating cubesats, including: companies, educational institutions, and government agencies
Due to standardization and the high risk tolerance of cubesat missions (i.e., the developers are willing to accept greater risks, or greater likelihood of mission failure), cubesats provide excellent educational opportunities and a relatively low-cost way to test new space hardware

## Slide 3: Foras Promineo Background
Foras Promineo is a 3U (10x10x30 cm3) cubesat Perkins High School (PHS) is developing
The 3U Foras Promineo cubesat payload is a small game with a robotic arm and free-floating game pieces contained inside an empty acrylic enclosure/structure – the game is currently undefined, but generally uses the arm to manipulate the game pieces within the acrylic enclosure to achieve some goal
Perkins successfully proposed the Foras Promineo mission to NASA’s CubeSat Launch Initiative (CSLI) solicitation – this provided the mission with funding for a launch (up to $300k in value)
Sierra Lobo is providing the electronics bus for the satellite and Perkins High School is building the payload – Sierra Lobo engineers also volunteer time working as mentors for Perkins’ robotics club and First Robotics Competition (FRC) team, which is developing the payload
The electronics bus for Foras Promineo contains components Sierra Lobo is interested in flying for future missions, including Sierra Lobo’s Bichromatic Littoral Temperature Observer (BaLTO) mission, a 12U cubesat with Long-Wave Infrared (LWIR) instrument meant to measure sea surface temperature for weather and climate modeling and prediction
Arm
End Effector
BaLTO CubeSat
Image taken with BaLTO LWIR sensor

## Slide 4: Foras Promineo Electronics – High Level
Foras Promineo’s electronics bus is based on the PyCubed architecture
The electronics bus contains lithium-ion batteries, solar cells, power management circuitry (for charging batteries and distributing power), a main printed circuit board (PCB) (with microprocessor for executing all spacecraft functionality), a LoRa radio (for payload data), an Iridium radio (for telemetry data), GPS (for position determination), antennas (for radio and GPS), custom PCBs (for interfacing with the payload), magnetorquers (for attitude control), inertial measurement units (IMUs) (for attitude determination), and a star tracker (TBR) (for attitude determination)
The main board runs a CircuitPython program that handles everything from power management, RF communication, telemetry collection, and attitude control to talking with the payload
The payload electronics consist of a couple custom PCBs to control the arm and payload bay lights as well as an OpenMV camera, which takes video of the payload and runs the game software
During gameplay, live video from the payload is transmitted to a ground station, which sends the video over the internet to the game web server. The game web server forwards this data to the person playing the game on their computer. Players use keyboard keys to control the arm in space. Data from their keyboards is sent back through the web server to the ground station, which transmits this control data back up to the satellite

## Slide 5: Space Operation
Satellite Software
Controls sat
Manages radio comms
Handles commands from Ground Station
Ground Station Computer
Send/Receive radio data from ground station
Sends payload data to website
Receives player input from Website
LoRa Ground Station
Sends and receives radio comms to/from satellite and ground station computer
Points ground station antenna at sat during flyover
Website
Shows “live” camera data
Allows user keyboard inputs

## Slide 6: Con-ops
Host PC software (for debugging and testing on the ground)
Ground Station PC Software
Ground Station LoRa software
Satellite Software
Website

## Slide 7: Helpful References
https://pycubed.org/
  Site for all things pycubed. Very good Documentation by Max Holliday
https://github.com/pycubed/forums/discussions
  Forms where a lot of people have asked relevant questions

## Slide 8: Preferred IDE for Satellite Coding
Visual Studio Code
  With Python extension and PyLint extension
    Pylint needs to be played with a little bit

## Slide 9: Using GitHub for code sharing
Installing GitHub desktop
Making a folder on your Z-drive
Forking the repository
Pushing changes to the master branch

## Slide 10: Satellite Software Preface
Satellite programming is mostly in CircuitPython. Firmware is written in C.
Satellite programming is for a MICROCONTROLLER, so it is MUCH less powerful and fast than a PC!!
  during normal execution there is <1MByte of RAM available for task execution.
  Floating point is MUCH slower than integer operations
  Data transactions over the radio are limited to 256 byte packets.
  UART interface to payload is running at ~115600 baud
Good practice is to just be mindful of what resources / typing your code is using.
  Since python is dynamically typed, type casting in this application is quite important!
    i.e. differences between a bool, int, float, char, and string object.
    Also be aware of various decorations like the 0x (hex) or b’’ (binary) prefix, or @property.setters

## Slide 11: Satellite Software Preface (cont.)
A lot of the background lower-level libs have been written by Max Alvarez (guy who developed PyCubed architecture) and Caden (me)

## Slide 12: Project File Structure
Top Level:
cdh, boot, and main files
Task Directory:
Tasks
Lib Directory:
All lib files for usage.

## Slide 13
Master Library
Init routine initializes each device in self.hardware
Each initialization for the devices is within its own try – except clause.
Hardware dictionary for each device in this library
Example device init.

## Slide 14
Master Library (cont.)
Reinit (very important)
Example of a property, i.e. class variable

## Slide 15
Master Library
Power mode setting

## Slide 16
Sub library example

## Slide 17
Anatomy of a Task
This is a task that blinks the led.
It is a subclass of task from template_task.py
When the task is executed, it runs the code within main_task.
Pycubed.py is self.cubesat
See priority and frequency for setting when a task will run.
To change priority and frequnency methods change_priority() and change_rate() must be called.
The mainboard executes tasks via a task scheduler

## Slide 18: template_task.py: the parent class to all tasks.
Some tasks may need a custom __init__ procedure
Every class can call debug() to print data to the terminal and optionally log it.
Load and save config are currently being tested. Not implemented for most tasks. These can be used for the cubesat to change task options mid-flight.

## Slide 19: Current Progress (as of 6/1/21)
Mainboard is functional and all peripherals are coded in.
  A new design revision will be made soon with some new features and some pinout changes.
Payload interface board libraries in progress
  ~90% complete, waiting on some parts and another design rev for the final design
Tasks have been started, but nothing of true substance there just trying to get a good background set up
Some PC/website software has been written.

## Slide 20: Things to Do:
Define operating states and what tasks should run at what times
Code high-level functionality
  i.e. all the tasks, commands, data handling
Define radio>mainboard>payload data exchange for target bitrate
Test it for extended periods extensively
Make sure all code written is executed successfully on ground
  Fault handling is EXTREMELY important in this application
Code pc host software to display live telemetry and simulate operations
Code PC ground station software

## Slide 21: Phase 1 Plan
Pair 1 will define and code simulation and data interface to host PC (main priority #2)
  We image a python program with a gui and real-time telemetry data updating, Marek started something like this but it really only uploaded new code to the device
Pair 2 will define and start to code the payload operation (main priority # 1)
  Will be discussed in a moment
Once host software is in a good state, it can start to be tested by Pair 1 Implementing the ADCS (main priority #3)
Prioritize a minimum-functional implementation before coding in more sophisticated functionality:
  For example, we would like to receive a stream of data from the openMV before there is error handling for dropped packets on the radio.

## Slide 22: USB Interface
Mainboard
Host PC
Usb_cdc.terminal
Usb_cdc.data
USB
Circuitpython REPL
All debug data is also printed here
Db_cdh and simulation handling
Circuitpython REPL terminal
Read debug data to display on GUI
Read/send cb_cdh and simulation commands

## Slide 23: Top Level Simulation / Debug Interface Flowchart

## Slide 24: REPL terminal and data stream
Regular circuitpython terminal.
Cubesat.debug prints data here
Print() command also prints here
Ctrl-C to end and ctrl-D to reload

## Slide 25: Debug command terminal
First asci encoded word “exec_cmd” is the keyphrase for the command to run
Then “ “ space for arguments passed
All arguments are separated by “arg0,arg1” comma right now, not “arg0, arg1“ comma space
Not implemented yet, but this is where the device will also ask for simulation data

## Slide 26: Main Operation Modes of Satellite
STARTUP MODE
SAFE MODE
IDLE MODE
PAYLOAD MODE
Each mode will have several substates.
Each mode/state will probably have specific tasks/ change task settings on the fly.
Runs once, x amount of time after initial deployment
Deploys deployables
Initial system checkout and startup
  i.e. ADCS detumble,
  ADCS calibrate,
  ETC.
Turns everything off, sleeps for x amount of time when it will re-check everything and try to re-enter idle mode.
Probably will beacon once for help during this. An override function may be implemented
Device in this mode most of time.
Will beacon over LoRa looking for commands from ground.
Payload will be powered off.
ADCS in point mode
Initiated from idle mode to start payload experiment.
Recieves data stream over LoRa for next arm/exec command
Sends data stream down of payload camera, arm, and important telemetry.
ADCS in payload_comp() mode, where it will hold and try to ignore arm torque exerted. (Low priority)
  If time, implement where cubesat will point at ground for better data transmission and reception.
I have a baseline experiment with a few free-running tasks right now, but this may need to be moved to a more discrete “frame”-like interface…

## Slide 27: STARTUP Mode
Wait x amount of time
Deploy antenna
Preform initial ADCS calibration
Do initial device checkout
Initiate first downlink

## Slide 28: Safe Mode
Turns all non-critical devices off.
Checks periodically for exit criteria to return to idle mode.
Will beacon SOS as a last resort

## Slide 29: Idle Mode
Will spend most time here.
ADCS will be running
Beaconing every so often to try to initiate contact with ground station

## Slide 30: Payload Mode
Checks Rx port for latest command data.
  Mostly user inputs from website
Sends data to payload and executes commands
When a photo is requested from GS, the sat will burst down a photo

## Slide 31: Over the Air (OTA)(Radio) Commands
Separate packet structures for 2 modes, beacon and connected.
RadioHead is the background library used by the GS and the sat. It does most of the handling for a header and ACK response.
The Satellite will receive commands from the ground-station less than 240bytes.

## Slide 32: Default “Beacon Mode” Radio Mode
Transmit Beacon
Recieve response?
No
Execute Command
Yes
Transmit Response

## Slide 33: Radio Packet Structure
RadioHead Header
4 Bytes
Command / response code
2 bytes
Args
Transmit / Receive both sides
Super Secret Code
X bytes
Command
2 bytes
…..
Our Header
2 bytes
If multi-packet flag,
4 bytes for packet counts
Our Packet:
Bytes 1-2 : Flags (i.e. listen again, last transmission, etc…)
  Idea: have a multi-packet flag for the radio to listen again and look for packet number bytes?
Bytes 3-4 : packet number
Bytes 5-6 : number of packets to send

## Slide 34: High-Speed “Connected” Radio Mode
Runs at frequency passed by start connected mode cmd
With a very short timeout also, ~0.5 sec

## Slide 35: Minimum Functionality (Payload)
Phase 1 goal overview

## Slide 36: adcs_task.py
Consult CryoCube code, Dr. Walker’s Dissertation, and Dr. Walker for details

## Slide 37: payload_task.py
Initated by command payload_start:
This only gets camera data from the openMV if the img_burst flag is true. Otherwise, it will do nothing.
  Other payload management tasks can go here
Img burst flag?
Send_buf flag?
Start
Place next chunk in buffer
Set send_buf flag
Yes
No

## Slide 38: db_cdh.py / usb_data_task.py
Debug commands sent via host PC
implement ability to run regular flight cdh.py commands with normal output over radio and debug info via USB.

## Slide 39: cdh.py
All of the “in flight” commands will go here.
setting persistent settings, imitating payload, printing log, printing telemetry, etc.
Some commands like exec, query, and hreset will probably have to be password-protected in addition?

## Slide 40: Radio tasks
Radios beacon unless they are “connected”
  Connection is a command sent where the GS specifies a frequency to check for new messages
  During this, they will explicitly listen unless prompted to burst data down by GS

## Slide 41: Telemetry gathering tasks
Imu_task.py
  Reads IMU data and overwrites data in cubesat.data_buffer{“imu”}.
GPS_task.py
  Reads GPS data and overwrites data in cubesat.data_buffer{“gps"}
Temperature_task.py
  Reads various temperatures and overwrites data in cubesat.data_buffer{“temp”}
  Turns overheating devices off.
Time_task.py
  Prints time data.
Battery_task.py
  Gathers battery information and power readings. Initiates safe mode if low battery is detected.

## Slide 42: Housekeeper task
Detects errors on satellite and attempts to fix them.
Preforms a daily hard reset to the satellite
Other housekeeping tasks?
  gc_collect is already its own thing running at 2Hz
Maybe separate this into its own error handling tasks
I’ve yet to decide if this should be one or many tasks…